## Slide 1: Physic’s Informed Reservoir Model
Arofenitra Rarivonjy
Akmuhammet Gurbangeldiyev

## Slide 2: Physic’s Informed Reservoir Model
Course: Technology of Science Informed Machine Learning
Technology of Science Informed Machine Learning
Term 5 , 2025
Arofenitra Rarivonjy
Akmuhammet Gurbangeldiyev
Term 5, 2025
Presented by

## Slide 3: Meet the team
Technology of Science Informed Machine Learning
Term 5 , 2025
Akmuhammet Gurbangeldiyev
Arofenitra Rarivonjy

## Slide 4: Introduction : Background
Technology of Science Informed Machine Learning
Term 5 , 2025
Reservoir simulation is critical for optimizing oil and gas production. PINN offers
Embedding physical laws directly into the loss function
Providing continuous solutions in space and time
Enabling efficient forward and inverse problem solving
Reducing computational cost for parametric studies

## Slide 5
Technology of Science Informed Machine Learning
Term 5 , 2025
Develop a PINN framework for reservoir pressure prediction
Implement physics-informed loss functions incorporating PDEs and boundary conditions
Train and validate models for single-well and multi-well scenarios
Compare performance and analyze pressure field characteristics
Scope of the Research :
This study focuses on 2D horizontal reservoir flow with incompressible fluid assumptions. The governing equation is the diffusivity equation, which describes pressure propagation in porous media.

## Slide 6: 2. Methodology
Technology of Science Informed Machine Learning
Term 5 , 2025
We model pressure dynamics in a 2D oil reservoir defined over the domain and time The governing PDE, a time-dependent diffusivity equation, is:
Where:
- : Pressure at position and time .
- : Permeability map, describing the ease of fluid flow through the reservoir rock.
- : Source term, representing oil production (negative for extraction) at well locations.
- Boundary conditions: No-flow (Neumann, on the domain boundaries.
- Initial condition: Uniform pressure (e.g., ).
For constant permeability

## Slide 7: Loss Function
Technology of Science Informed Machine Learning
Term 5 , 2025
Data Loss:
PDE Loss:
IC Loss:
Total Loss:
BC Loss:

## Slide 8: Implementation
Technology of Science Informed Machine Learning
Term 5 , 2025
Pytorch implementation with automatic differentiation
Neural network : MLP [3] → [40] → [40] → [40] → [1] , with tanh activation functions
Collocation Points: Randomly sampled points (e.g., 1000 points) to evaluate the PDE residual.
Permeability: Currently a constant , but designed to handle a grid-based map via interpolation (e.g., using scipy.interpolate.griddata).
Well Source: A Gaussian source term represents a production well at (0.5, 0.5).
Boundary Sampling: Neumann conditions are enforced by penalizing normal derivatives at boundary points.
Data Points: Placeholder data (e.g., at can be replaced with real measurements.

## Slide 9: Implementation
Technology of Science Informed Machine Learning
Term 5 , 2025
Optimizer: AdamW with initial lr 1e-3 and weight_decay of 1e-4
Learning rate schedule: Step decay (γ = 0.5 every 5000 epochs)
Collocation points: 1000 (single well) to 1500 (multiple wells) randomly sampled per epoch
Training epochs: 15,000 for both scenarios
Data augmentation: Synthetic pressure measurements (20-30 points) with noise
Sparse pressure measurements are generated using:

## Slide 10: 3. Results : Single Well Scenario
Technology of Science Informed Machine Learning
Term 5 , 2025

## Slide 11: 2 Wells Outside
Technology of Science Informed Machine Learning
Term 5 , 2025

## Slide 12: 3 Wells scenario
Technology of Science Informed Machine Learning
Term 5 , 2025

## Slide 13: 4 wells scenario
Technology of Science Informed Machine Learning
Term 5 , 2025

## Slide 14: Comparison of scenarios
Technology of Science Informed Machine Learning
Term 5 , 2025
Metric | 1 well | 2 wells | 3 wells | 4 wells
Total Loss | 3.748e-3 | 1.2e-5 | 4.25e-2 | 0.055145
Training time | 15 min | 16 min | 15 min | 14 min
Min Pressure (t=1.0) | 0.8692 | 0.999955 | 0.918 | 0.9312
Pressure Gradient | Uniform Radial | Complex | Complex | Complex
Data Points Used | 20 | 30 | 30 | 30
Collocation Points | 1000 | 1500 | 1500 | 1500

## Slide 15: 4. Discussion and Analysis : Strength of PINN
Technology of Science Informed Machine Learning
Term 5 , 2025
Physics Integration : Embedding the diffusivity equation into the learning process
Mesh-Free Solution (unlike finite element method)
Handling complex well configurations
Inverse Problem capability (Estimating k(x,y) from pressure)
4. Discussion and Analysis : Limitations of PINN
Computational Cost
Loss balancing (hyperparameters finetuning)
Can stuck in local minima
Sharp gradient near well

## Slide 16: PINN VS Traditional Methods
Technology of Science Informed Machine Learning
Term 5 , 2025
Aspect | PINN | Finite Difference
Setup Time | Low (no meshing) | Medium (grid setup)
Accuracy | Good (with sufficient training) | High (stable schemes)
Computational Cost | Medium (training) | Low (single solve)
Inverse Problems | Natural | Difficult (adjoint)
Adaptivity | Easy (resampling) | Hard (regridding)
Data Integration | Seamless | Post-processing

## Slide 17: Connection to PINO Framework
Technology of Science Informed Machine Learning
Term 5 , 2025
This work implements PINN (point-wise evaluation) but shares philosophy with Physics-Informed Neural Operators (PINO):
PINN (this work):
Learns mapping: (x, y, t) → p
Requires retraining for new permeability k or well configuration
PINO (future extension):
Learns operator: k, q → p (function → function)
Generalizes to new permeability maps without retraining
Combines Fourier Neural Operators (FNO) with physics loss

## Slide 18: Extension to more complex cases
Technology of Science Informed Machine Learning
Term 5 , 2025
Sine activation networks (improved spectral propriety)
Heterogeneous permeability fields
Mixed well configurations
Curriculum learning (begin from 1 well to several wells)
where:
φ = 0.2: Porosity (constant)
μ = 1.0: Fluid viscosity
c_t = 10⁻³: Total compressibility
k(x,y): Spatially-varying permeability
q(x,y,t): Time-dependent source term

## Slide 19: Sine vs standard
Technology of Science Informed Machine Learning
Term 5 , 2025
Total Loss: 13.327844
PDE: 13.327836,
BC: 0.000005,
IC: 0.000002
LR: 3.78e-07,
Network: standard
Total Loss: 12.456
PDE: 12.453490,
BC: 0.002154,
IC: 0.000729
LR: 3.78e-07,
Network: sine

## Slide 20: Sine vs standard
Technology of Science Informed Machine Learning
Term 5 , 2025

## Slide 21: Summary
Technology of Science Informed Machine Learning
Term 5 , 2025
This Project presents the development and application of Physics-Informed Neural Networks (PINNs) for predicting pressure dynamics in oil reservoirs. The approach combines neural network learning with physical laws (partial differential equations) to model fluid flow in porous media. Two scenarios are investigated: single-well and multi-well configurations. Results demonstrate that PINNs can effectively capture complex pressure distributions while respecting underlying physics.

## Slide 22: 5. Conclusion
Technology of Science Informed Machine Learning
Term 5 , 2025
- We successfully provide mathematical formulation, PINN Implementation, Physics informed loss, single well and multiple well success and visualization.
Physics integration enable accurate predictions, mesh-free approach, scalable from single to multiple well, converge in 30 000 epochs, interpretable.
Practical Implications : Real time forecasting, uncertainty quantifications, optimizations, history matching, etc .
5. Future Research Directions
Model enhancements in several cases
Use of advanced architectures NN or NO
Use in real case study

## Slide 24: References
Li, Z., Kovachki, N., Azizzadenesheli, K., Liu, B., Bhattacharya, K., Stuart, A., & Anandkumar, A. (2021). Fourier Neural Operator for Parametric Partial Differential Equations. arXiv:2010.08895.
Li, Z., Zheng, H., Kovachki, N., Jin, D., Chen, H., Liu, B., Azizzadenesheli, K., & Anandkumar, A. (2023). Physics-Informed Neural Operator for Learning Partial Differential Equations. arXiv:2111.03794.
Raissi, M., Perdikaris, P., & Karniadakis, G. E. (2019). Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations. Journal of Computational Physics, 378, 686-707.
Aziz, K., & Settari, A. (1979). Petroleum Reservoir Simulation. Applied Science Publishers.
Wang, S., Teng, Y., & Perdikaris, P. (2021). Understanding and mitigating gradient flow pathologies in physics-informed neural networks. SIAM Journal on Scientific Computing, 43(5), A3055-A3081.